## Slide 1: Why Nuclear?: System Role, Costs, Safety, and Perception
Victor Ibarra, Senior Manager for the Advanced Nuclear Energy Program, Clean Air Task Force June 9th , 2026
Confidential & Not for Distribution

## Slide 2: Nuclear has become popular again
Private industry is procuring new (and reviving old) nuclear in the US:
  Google has procured 500 MW of advanced nuclear from Kairos Power.
  Dow Chemicals and X-Energy signed a joint development agreement for four Xe-100 units.
  Amazon funded Cascade Advanced Energy Facility in Washington plans for 12 X-Energy reactors.
  Microsoft signed a deal to revive 835 MW Three Mile Island nuclear power plant.
  NRC authorized Palisades (800 MW) to restart.
In New York State, Gov. Hochul has directed the New York Power Authority (NYPA) to develop and construct no less than 1 GW advanced nuclear power in Upstate New York.
Illinois executive order by Gov. Pritzker will support the deployment of new nuclear facilities with a goal of "delivering at least two gigawatts of new clean nuclear capacity."
“Tennessee Valley Authority Tennessee signed agreement for 6 GW of new nuclear.
In 2025, the U.S. government announced an $80 billion partnership with Westinghouse Electric Company, Brookfield Asset Management, and Cameco Corporation to deploy a new fleet of AP1000 nuclear reactors
Globally, over 60 reactors are under construction.
Confidential & Not for Distribution

## Slide 3: What Role Might Nuclear Play for Decarbonization?
Before we dive in, it should be emphasized that there is a need to massively expand renewables, transmission, and storage under all futures with and without nuclear…
But there are three perspectives we should consider for assessing the role of nuclear:
Clean supply optionality
Lessening the infrastructure buildout challenge to achieve decarbonization
Lowering the system cost of decarbonization
Confidential & Not for Distribution

## Slide 4
Clean Firm Reduces Enormous Buildout Needed to Decarbonize
Confidential & Not for Distribution
California Decarbonization – 2050 Results
Germany Decarbonization – 2050 Results
Source: Long et al. (2021). Clean firm power is the key to California’s carbon-free energy future. Issues in Science and Technology. https://issues.org/california-decarbonizing-power-wind-solar-nuclear-gas/
Source: Quantified Carbon. (2025). Clean Firm Power in Europe’s Energy Transition. https://cdn.prod.website-files.com/650ac0ab00dff792a8cebc3c/6978eef2e54578d3f5da976f_CATF_4%20Report.pdf
~300 GW
~250 GW

## Slide 5: Cost Savings More than Clean Firm Cost
Confidential & Not for Distribution
Diff. in Annual Investment between Scenarios ($B/yr)
Chart: 
| 2030 | 2035 | 2040 | 2045 | 2050
RE | -24.3673 | -100.9207 | -185.8072 | -295.8641 | -456.8013
Nuclear | 3.4016 | 20.0852 | 43.4882 | 84.1492 | 149.7021
Battery | -1.1444 | -5.1469 | -9.7275 | -9.083 | -9.9571
Other, incl. NG-CCS | 6.4259 | 6.7762 | 11.7105 | 17.633 | 23.9634
T&D | -0.84616 | -8.9116 | -26.2423 | -64.7432 | -110.3737
Bioconversion | 0.020844 | 15.4057 | 9.2215 | -1.3986 | -77.0165
H2 Prod | 3.2362 | -7.2207 | -43.5857 | -104.8604 | -190.0351
CO2 T&S | 3.4496 | 15.7313 | 28.4992 | 43.7464 | -5.9368
Nat Gas Infra | 0.03902 | 0.15731 | 0.23532 | 0.29683 | 0.36461
Oil Delivery | -2e-06 | -3e-06 | -4e-06 | -5.5e-05 | 0
RE+Storage
Nuclear
T&D
CCS
Bio
H2
CO2 T&S
More costs in E+RE- Scenario
More costs in E+RE+ Scenario
Notes: Investment costs differences in Princeton’s Net Zero America between the E+RE- and E+RE+ scenarios, showing how additional nuclear and CCS investment can offset a disproportional amount of renewable, transmission, and H2 cost.
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
E+RE- Minus E+RE+ | -0.54 | -1.69 | 3.81 | -15.17 | -96.91 | -216.83 | -524.7
More costs in E+RE- Scenario
More costs in E+RE+ Scenario
Diff. in Total Costs between Scenarios ($B/yr)

## Slide 6: Large and small light water reactors enable near-term deployment of larger new nuclear reactors
Confidential & Not for Distribution
GEH BWXR-300
Targeted deployment of first reactor by 2028 at Darlington, Canada site
Up to 4 units deployed by OPG
Additional units may be built in U.S. by TVA, Duke, and Dominion
Holtec SMR-300
Targeted deployment of two reactors by 2030 at Palisades site
Additional units may be deployed in United Kingdom or Canada
Westinghouse AP1000
2 reactors operational at Vogtle 3&4
2 reactors announced for completion at V.C. Summer in South Carolina
4 reactors announced at Fermi America and Project Matador in Texas
$80B of new AP1000s under discussion

## Slide 7: Non light-water advanced reactors leverage new reactor technologies and fuels to enter new markets
Confidential & Not for Distribution
TerraPower Natrium
345 MWe/ 840 MWth sodium cooled reactor with thermal energy storage
Capable of ramping between 100 MWe and 500 MWe of electricity output
First customers will be PacifiCorp and Microsoft
Kairos Power Hermes
50 MWe/ 125 MWth molten salt reactor with TRISO fuel pebbles
Received construction permit for two demonstration reactors
First customers will be Tennessee Valley Authority and Google
X-Energy Xe-100
80 MWe/200 MWth modular high temperature gas reactor
Commercial operation for combined heat and power production
First customers will be Dow Chemical, Energy Northwest, and Amazon

## Slide 8: Microreactors for energy or heat production could meet the needs of individual users or microgrids
Confidential & Not for Distribution
Radiant Kaleidos
1 MWe/3 MWth modular high temperature gas reactor
Highly deployable for remote power
Testing planned at INL in 2027
First customers will be U.S. Air Force at unnamed U.S. base in 2028
BWXT BANR
15 MWe/50 MWth modular high temperature gas reactor
Builds on Project Pele transportable microreactor project for DoD
Planned initial deployment in Texas and Wyoming by 2029
Aalo Aalo-X
10 MWe/30 MWth sodium cooled fast reactor
Builds on Idaho National Lab (INL) MARVEL reactor concept
Testing planned at INL in 2026

## Slide 9: Analysis of best practices and learning by doing suggest substantial cost reductions over time for nuclear energy
Idaho National Lab Study on Future Advanced Reactor Costs
INL cost study conclusions:
Lower initial costs for standardized large reactors with 23 – 57% cost reductions from widescale deployment
Higher initial costs for standardized SMRs with 38 – 64% cost reductions from factory manufacturing
Confidential & Not for Distribution
Large Nuclear Reactors
Small Modular Reactors
2030
2040
2050
2030
2040
2050
$/kWe CapEx (2022 Dollars)
Vogtle 3 & 4
Actual
Best Practices
2022
$14,000
$16,000

## Slide 10: Nuclear safety, nuclear risk, and nuclear regulation are ultimately social, political, and technical processes
Societal views on activity hazards, harms, trade-offs, risks, and stakeholders
Political acceptance of trade-offs, response to stakeholders, and assessment of technical considerations
Scientific and engineering evaluations of hazards, harms, trade-offs, and risks
Social Considerations
Political Considerations
Technical Considerations
Should regulations should consider the impacts of different comparable technologies or cost/benefits?